## Slide 1: Car Indicators Requirements
Draft Version

## Slide 2: Context Diagram
Car Indicators
Step_Down_BTN
Step_Up_BTN
Hazzard_BTN
Left_SSD
Right_SSD

## Slide 3: Interfaces
ID | System Interface | HW Interface
01 | Step_Down_BTN | S2
02 | Step_Up_BTN | S3
03 | Hazzard_BTN | S4
04 | Left_SSD | SSD above S3
05 | Right_SSD | SSD above S4

## Slide 4: 06 - System State M/C
Idle
Hazzard
Left
Right
Step_Down
Step_Up
Step_Up
Step_Down
Hazzard [Idle]
Hazzard
Hazzard
Hazzard [Left]
Hazzard
Hazzard [Right]

## Slide 5: Hazzard State
07- To enter/exit this state, Hazzard_BTN must be released after a press >= 200 ms.
08- When entering, store previous state.
09- On exit, previous state must be restored.
10- In this state, both SSD should blink the letter ‘8’.
11- ON time = 200 ms ± 10 ms
12- and OFF time = 400 ms ± 10 ms.

## Slide 6: Idle State
13- Initial state and both SSD should be OFF.
14, 15- Go to Left/Right if Step_Down_BTN/Step_Up_BTN is pressed for >= 10ms.
16- Go to Hazzard if Hazzard_BTN is released after a press >= 200 ms.

## Slide 7: Left State
17- In this state, Left_SSD should blink the letter ‘8’.
18- ON time = 200 ms ± 10 ms
19- and OFF time = 300 ms ± 10 ms.
20- Go to Idle if Step_Up_BTN is pressed for >= 10ms.
21- Go to Hazzard if Hazzard_BTN is released after a press >= 200 ms.

## Slide 8: Right State
22- In this state, Right_SSD should blink the letter ‘8’.
23- ON time = 200 ms ± 10 ms
24- and OFF time = 300 ms ± 10 ms.
25- Go to Idle if Step_Down_BTN is pressed for >= 10ms.
26- Go to Hazzard if Hazzard_BTN is released after a press >= 200 ms.

## Slide 9: Special Requirements
27- In case of simultaneous button events, the following priority must be enforced:
  Hazzard_BTN
  Left_BTN
  Right_BTN

## Slide 10: Car Indicator Architecture
Draft

## Slide 11: Car Indicators Block Diagram
Step_Down_BTN
Step_Up_BTN
Hazzard_BTN
Left_SSD
Right_SSD
Button
SSD
GPIO
sEOS
Controller
HIF
TIF

## Slide 12: Requirements Allocation
Module | Requirements IDs
GPIO | 01 – 05
Buttons | 01 – 03, 07, 14 – 16, 20 – 21, 25 – 26
SSD | 04 – 05, 10, 13, 17, 22
Controller | 06 – 10, 13 – 17, 20 – 22, 25 – 27
HIF | 10 – 13
TIF | 13, 17 – 19, 22 - 24

## Slide 13: Timing C/C’s
Task/OS | Timing C/C’s | Period/Tick
Button | 20 ms | 20 ms
Controller |  | 20 ms
HIF | 200 ms, 400 ms | 200 ms
TIF | 200 ms, 300 ms | 100 ms
sEOS |  | 20 ms

## Slide 14: Time Line - 200 ms
Button
Controller
HIF
TIF
Note that HIF and TIF responsiveness is not good. To improve it, decrease their periods but will increase CPU load.  Periods will be 20 ms for all tasks as a start.